## Slide 1: Free-Space Optics in Data Centers
Acknowledgement for Slides: Navid Hamed Azimi

## Slide 2: Datacenter network design is hard!
Cost
Performance
Cabling
Expandability
Energy
Cooling
Adaptability
Notes: Transition to the next

## Slide 3: Existing Choices
Over subscribed
(tree, leaf spine,…)
Performance
Cost
…
Core
Top of Rack (ToR)
Notes: VS: – make cost performance higher size .. Move stuff above .. Avoid stuff close to bottom – change upper layers to “core”. Animate the order of appearance

## Slide 4: Existing Choices
Over subscribed
(tree, leaf spine,…)
…
Over provisioned
(Fattree, Jellyfish,…)
Performance
Cost
Top of Rack (ToR)
Core
Notes: VS: please fix slide 4/5 to be in tune with formatting on slie 3

## Slide 5: Existing Choices
…
Core
Over subscribed
(tree, leaf spine,…)
Performance
Cost
Augmented
(c-Through , 3D Beam)
Top of Rack (ToR)
Over provisioned
(Fattree, Jellyfish,…)
Notes: VS: Increase font of can we get here

## Slide 6: Existing Choices
Over subscribed
(tree, leaf spine,…)
Performance
Cost
Augmented
(c-Through , 3D Beam)
Over provisioned
(Fattree, Jellyfish,…)
Can we get here?
Notes: VS: Increase font of can we get here

## Slide 7: Our Vision
…
Core  Coreless
Wired  Wireless
Static  Flexible

## Slide 8: Potential Benefits of This Vision
Cost
Performance
Cabling
Expandability
Energy
Cooling
Adaptability
Wireless
Coreless
Flexible
Notes: Transition to the next

## Slide 9
Challenges in Realizing the Vision
Flexible wireless links
Network management

## Slide 10
Outline
Flexible wireless links
Network management
Feasibility & cost

## Slide 11: Traditional RF is not Sufficient
…
Wide beam
High interference

## Slide 12: Traditional RF is not Sufficient
…
Wide beam
Difficult to narrow
High interference

## Slide 13: Solution: Free Space Optical Links (FSOs)
No interference
High throughput
over long range
…
Easy to narrow beam

## Slide 14
Concerns with FSOs
Cost : $30K
Size : 3 ft³
Power: 60w
Flexibility
Notes: VS: animate for effect. Show the picture and then emphasize the key things

## Slide 15: Why Size, Cost, Power Can be Reduced?
Traditional use : outdoor, long haul
  High power
  Weatherproof
Data centers: indoor, short haul
  Low power
Feasible roadmap via commodity fiber optics
  E.g. Small form transceivers (Optical SFP)

## Slide 16: Proof of Concept (1 Gbps) (shown by Navid et.al in Hotnets’13)
Fiber connected
to SFP (TX)
Lens
Lens
Mirror
Mirror
SFP (RX)
SFP : 2x$40
Lens : 2x$30
Notes: Pause and say the take away (We have build it cheaply with commodity components with small size)

## Slide 17: FSO Link Throughput (shown by Navid et.al in Hotnets’13)
Chart: 
| <924 | 924- 928 | 928- 932 | >932 Mbps
Optical fiber | 0.015 | 0.215 | 0.87 | 0
FSO | 0.015 | 0.217 | 0.868 | 0
PDF
Throughput
FSO link is the same as optical cable

## Slide 18: FSO Link Misalignment Tolerance
Effect of vibrations, etc.
Movement tolerance
  0.7mm at destination
  3mm at source
3 mm
0.7 mm
FSO link is stable
TX
RX

## Slide 19
Cost : $30K
Size : 3 ft³
Power: 60w
Flexibility
FSOs (1Gbps)
Cost : $140
Size : 1x4 in
Power: 0.3w
Flexibility
Notes: Change the architecuter

## Slide 20: Flexibility via Switchable Mirror
Sender
Ceiling Mirror
Receiver 1
Reciever2
Switchable Mirror: glass mirror
Electronic control, low latency
SM in “mirror”
mode

## Slide 21: Flexibility via Switchable Mirror
Sender
Ceiling Mirror
Receiver 1
Reciever2
SM in “mirror”
mode
Receiver 1
Reciever2
Switchable Mirror: glass mirror
Electronic control, low latency

## Slide 22
Outline
Flexible wireless links
Network management
Feasibility & cost

## Slide 23: Management: Pre-Configuration
Input: FSO#, SM#,…
23
Sender
Receiver 1
Reciever2
Output: Candidate links (Alignment of each SM)
Notes: Candidate topology vs Runtime Topology

## Slide 24: Management: Reconfiguration
Input: Traffic
24
Sender
Receiver 1
Reciever2
Output: Run-time topology
Notes: Candidate topology vs Runtime Topology

## Slide 25: Current Solutions: Simple Heuristics
Pre-Configuration : Regular Random Graph
Reconfiguration
  Only reconfigure for large flows
  Only delete a link if network remains connected

## Slide 26: Goal
How does FSO-based DC compare in terms of end-end performance with other DC topologies like Fattree, JellyFish, Cthrough, 3-D beamforming etc.?
How do we ensure consistent updates across reconfigurations? Properties we want to satisfy:
  No black holes
  End-End connectivity
  Bounded latency

## Slide 27: Evaluation Plan
htsim: packet level simulator
  End-End performance comparison with other DC topologies
  Consistent updates across reconfigurations
Mininet:
  Consistent updates across reconfigurations
fs: flow level simulator
  Scalability i.e., end-end performance with >=1000 racks

## Slide 28: htsim: End-End Performance

## Slide 29: htsim: Dynamics Link and Route Updates

## Slide 31: Mininet: End-End Performance

## Slide 32: Mininet: Route and Link Dynamics

## Slide 33: Mininet: Parameters

## Slide 34: FS: Parameters

## Slide 35: Fs: End-End Performance

## Slide 36: Fs: Scalability

## Slide 37: TO DO
Implement consistent update algorithms in htsim and mininet
Properties
  No Black Holes
  End-End Connectivity
  Bounded Latency
End-End Performance with
  Packet Scattering
  Other Data center topologies
fs: End-End performance tests for 1000 rack topologies